## Slide 1: DPRS/TRAINSET
SIDDHARTH SHANKAR
P(Trainset)/IRIMEE

## Slide 2: What is a DPRS ?

## Slide 3: DPRS
Stands for Distributed Power Rolling Stock
Class of vehicles fit to move on Railway systems and one where the Propulsion systems and Powered wheels for providing tractive force are distributed over more than one and mostly large number of vehicles
This is opposed to locomotive hauled trains where the equipment and powered wheels producing Tractive effort are contained in vehicle/ vehicles which are non-passenger carrying and are coupled to passenger cars through mechanical coupling

## Slide 4: Concentrated Power train
Distributed Power train
Locomotive
Motor coach
Coach
Coach
Coach
Coach
Coach
Coach
Coach
Coach
Coach
Coach
Coach
Motor coach
Coach
Coach
Motor coach
Coach
Coach

## Slide 5
Internal Power Source - Diesel Electric and Multiple Unit with AC-DC or AC- AC Drive or Hydraulic Drive.
External Power source - EMU/ MEMU Train sets drawing power from AC OHE with DC Motors or AC Motors OR DC OHE or third rail with AC Motors.
TYPES ON THE BASIS OF POWER SOURCE
Hybrid – Combination of Internal and external power source

## Slide 6: DELHI METRO

## Slide 7: SHINKANSEN
100 % powered trainset
All axles in a bullet train are propelled by a traction motor

## Slide 8: CONCEPT OF TRACTION

## Slide 9
Peak Power Curve

## Slide 10
Adhesion Limit

## Slide 11
Why is there an Adhesion Limit?

## Slide 13
The Law of Rail Traction

## Slide 14
Speed Limit

## Slide 15
Why is there a Speed Limit?

## Slide 16: Other Factors Limiting Maximum Speed
Bearing Design
Vibrations
Mechanical Transmission System
External - Tracks and Structures

## Slide 17
Tractive Effort of a Powered Rolling stock

## Slide 18
Resistance to Movement of Rolling Stock

## Slide 20: Aerodynamic drag of a typical train
Bogie and wheels
45.5%
Surface friction from sides and roofs
27%
Front
4.5%
Tail
3.5%
Under floor equipment
7.5%
Ventilation etc
4%
Pantographs
8%

## Slide 22
Vehicle Design to Minimise Air Drag

## Slide 23
Achieving High Speed
Aerodynamic Design
For high speeds, air drag is to be minimized.
Aerodynamically designed Car body with long nose to reduce drag
When high speed train exits a tunnel, a blasting sound is generated due to micro pressure waves. To reduce this micro pressure, the front car is designed with a nose section.

## Slide 24: AERODYNAMIC BODY DESIGN

## Slide 25
Achieving High Speed
Side and Bottom covers for Bogies and other underframe mounted equipment
Fairings fitted all around the gaps between cars
Reducing Air Drag

## Slide 26: Why Distributed Power ?
6𝐹𝛼- (D+𝑇𝑟 )= 𝑚𝑡𝑟 𝑎𝑥
6𝛼𝑃𝑖- (D+𝑇𝑟 )= 𝑚𝑡𝑟 𝑎𝑥
𝑛𝛼𝑃𝑖- (D+𝑇𝑟 )= 𝑚𝑡𝑟 𝑎𝑥
𝛼𝒏𝑷𝒊- (D+𝑇𝑟 )= 𝑚𝑡𝑟 𝑎𝑥
More adhesive mass in case Of DPRS
n- number of powered axles 𝛼- adhesion coefficient 𝑃𝑖 – Axle load 𝐹𝛼 - adhesive mass
D – Rolling resistance, drag resistance etc 𝑇𝑟 - Trailing load
From above equation it is clear that greater is the number of powered axles, Greater is the adhesive mass and hence better acceleration

## Slide 27: Distributed Power/Concentrated Power
The distributed traction system has many advantages
  energy efficiency
  light axle weight
  high acceleration and deceleration due to large number of driving axles
  more cabin space as there are no
locomotives
  and ability to utilize the energy of regenerative braking efficiently
Ref: Akiyama et al.

## Slide 28: DPRS Types in Indian Railways
Diesel Multiple Units-DMU/DEMU
Electrical Multiple Units-EMU
Mainline Electrical Multiple Units-MEMU
Trainsets - High Speed
Train sets -Semi High Speed

## Slide 29: Trainset – Semi High Speed T-18
Train-18 is 16 car train with 4 basic unit i.e. Two number of end basic unit (DTC-MC-TC-MC) and two number of middle basic unit (NDTC-MC-TC-MC)
Semi-high speed (160 kmph) multiple unit train-set.
Train-18 is provided with IGBT based energy efficient 3 phase propulsion system and regenerative braking
Stainless steel car body with continuous window glasses
All propulsion equipments are shifted from onboard to under-slung. All power components such as line & traction converters, auxiliary converter, air compressor, battery box, battery charger, brake chopper resister are mounted under the frame
Zero discharge vacuum-based bio-toilets
Modern bolster-less design bogies with fully suspended traction motors,
Train-18 has 50% powering i.e. Every alternate coach is powered
Ethernet backbone

## Slide 30: Trainset -High Speed
Operational speed greater than 200 Kilometer per hour on existing track
Operational speed greater than 250 Kilometer per hour on new track
Significantly faster than traditional railway trains
E.g.- Bullet Train (Japan)
- ICE (Germany)
- TGV (France)
- CRH (China)

## Slide 31: Rolling stock requirement
Self propelled, fixed composition and bi-directional
High level of technology
Limited axle load High traction power 3 Phase Propulsion System
Power electronic equipment: GTO, IGBT based Control circuits
Computer network- centralised train control system
Automatic diagnostic system
Optimised aerodynamic shape
In-cab signalling system/s
Several complementary braking systems
Airtight structure
High level of RAMS (Reliability, Availability, Maintainability and Safety)

## Slide 32: Advantages of Trainsets
Better acceleration and deceleration
Saving in run time
Energy efficient
Enhanced safety
Reduced maintenance
Improved reliability
Reduction in pollution
Improved passenger comfort
Improved line capacity
Designed to handle super dense crush load

## Slide 33: Enhanced safety
Most DPRS have regenerative and Electro pneumatic braking features, Emergency braking distance is reduced
Reduce jerks due to smoother acceleration and deceleration due distributed power and traction forces
Anti-telescopic design

## Slide 34: Reduced maintenance
Reduced wear of track and wheels since power is distributed
Regenerative & EP braking improves wheel life
3 phase IGBT VVVF propulsion
AC traction motor

## Slide 35: Improved reliability
3 phase IGBT technology is highly reliable
Distributed powering has a lot of in built redundancy, since 50-60 % of axles are powered.
Man machine interface gives apt feedback about any issues in the propulsion system.
In-built fault diagnostics.

## Slide 36: Improved line capacity
Faster acceleration & deceleration leads in time required to clear a critical section
Higher carrying capacity of DPRS will reduce number of trains required for same throughput.

## Slide 37: THANK YOU